## Slide 1
Drainage line chattering?
Yes
Evaluate for
- hypovolemia
- cannula malposition/obstruction
- tension PTX, cardiac tamponade
No
Any recent change to
ECMO or ventilator settings?
Adjust ventilator or ECMO setting as appropriate
Yes
Check color of return line:
same as drainage line?
1. Return line blood gas analysis
2. Change oxygenator
Yes
Increased CO?
e.g. fever, tachycardia, agitation/delirium
1. Treat any fever/pain
2. Consider sedation, paralysis, beta-blockade
Yes
Worsened native lung function?
1. Lung exam, chest radiograph
2. Increase ECMO setting
Yes
Decreased SvO₂?
1. Evaluate for sepsis, cardiac failure, anemia
2. Increase ECMO setting
Yes
Sudden desaturation
i.e. ≥ 10% SaO₂ decrease from baseline
No
No
No
No

## Slide 2
배액관 떨림(chattering)?
예
다음을 평가:
- 저혈량증
- 캐뉼러 위치 이상/폐색
- 긴장성 기흉, 심낭압전
아니요
최근 ECMO 또는 인공호흡기 설정 변경?
인공호흡기 또는 ECMO 설정을 적절히 조정
예
관류 캐뉼라 혈액색 확인:
배액 캐뉼라와 동일한가?
1. 관류 캐뉼라의 혈액가스 분석
2. 산소기 교체
예
심박출량 증가?
예. 발열, 빈맥, 초조/섬망
1. 발열/통증 치료
2. 진정, 근이완, 베타차단제 고려
예
환자의 폐 기능 악화?
1. 폐 청진, 흉부 방사선 촬영
2. ECMO 설정 증가
예
혼합정맥 산소포화도 감소?
1. 패혈증, 심부전, 빈혈 평가
2. ECMO 설정 증가
예
갑작스러운 산소포화도 저하
예. 기저치 대비 산소포화도 ≥ 10% 감소
아니요
아니요
아니요
아니요