## Slide 1
Keep higher RPM
Change to larger cannula or
insert additional drainage cannula
Reposition cannula
Severe ARDS on VV ECMO
Set target SaO₂
(Under protective ventilator setting)
Moderate to Light sedation
80 – 88%
Awake
> 88%
Titrate ECMO flow ≥ 60% of cardiac output
(i.e. 60-80ml/kg/min)
Unable to get target SaO₂
Check pre-oxygenator SaO₂
< 80%
80 – 90%
> 90%
Reposition cannula to decrease recirculation
Test increase of ECMO RPM (~20%)
Flow & SaO₂ increase
Flow unchanged
Flow increases,
but SaO₂ unchanged

## Slide 2
높은 RPM 유지
더 큰 캐뉼라로 교체 또는
추가 배액 캐뉼라 삽입
캐뉼라 위치 조정
VV ECMO 중인 중증의 급성 호흡곤란 증후군
목표 산소포화도 설정
(보호 환기 설정 하에서)
중등도-경증 진정
80 – 88%
각성
> 88%
심박출량의 ≥ 60%로 ECLS 유량을 조절
(i.e. 60-80ml/kg/min)
목표 산소포화도 달성 불가
산화기 유입 전 정맥 산소 포화도 측정
< 80%
80 – 90%
> 90%
재순환 감소를 위해 캐뉼라 위치 조정
ECLS RPM 증량 시도 (~20%)
유량 및 산소포화도 증가
유량 변화 없음
유량은 증가하나
산소포화도는 변화 없음